## Slide 1: Lab Safety, Symbols & Equipment
Packet #2

## Slide 2: Chemical Symbols
Symbols Located on Chemicals

## Slide 3: Chemical Symbols I
Yellow
  Reactivity

## Slide 4: Chemical Symbols II
Red
  Severe Hazard/Flammability

## Slide 5: Chemical Symbols III
Blue
  Health

## Slide 6: Chemical Symbols IV
White
  Special Hazard

## Slide 7: NFPA CHEMICAL HAZARD LABEL
Avoid water.
May detonate with heat or ignition.
Severe health risk.
Burns readily.
Diborane

## Slide 8: MSDS

## Slide 9: MSDS I
Material Safety Data Sheet
  On file for all purchased chemicals
  Includes information on chemical label
  Different formats are used by different companies

## Slide 10: MSDS II Example

## Slide 11: Laboratory Safety Symbols

## Slide 12: Laboratory Safety Symbols I
Students should be familiar with all symbols

## Slide 13: Laboratory Safety Symbols II
Students should be familiar with all symbols.

## Slide 14: Laboratory Safety Symbols III
Students should be familiar with all symbols.

## Slide 15: Lab Safety Rules

## Slide 16: Goggles
Students are required to wear safety goggles at all times during lab exercises.
Failure to wear safety goggles could result in chemical burns of the eye.

## Slide 17: Hair
Hair must be tied during lab exercises.

## Slide 18: No Backpacks
Backpacks and purses are not allowed in the lab area.

## Slide 19: Things to Know…
Know the locations of
  Eyewash
  Fire Blanket
  Fire Extinguisher

## Slide 20: No Horseplay
No horseplay in the lab area!

## Slide 21: No Food/Drink
No food or drink in the lab area.

## Slide 22: No…
No unauthorized experiments!

## Slide 23: Removal of Lab Equipment
Never remove chemicals or lab equipment from lab.

## Slide 24: Unlabeled Containers…
Never use chemicals from an unlabeled container.

## Slide 25: Heating Test Tubes
NEVER point the mouth of a test tube or Erlenmeyer flask at yourself or another person!
ALWAYS direct the mouth away from people!
Correct!
Wrong!

## Slide 26: Heating Containers…
Never heat a closed container.
  Pressure in container increases and can cause chemicals to spray out from the top or cause the contained to shatter spreading shards of glass.

## Slide 27: Flammable Substances
Keep ALL flammable substances from heat sources/open flames.
Never heat a liquid in a test tube over an open flame; use a water bath.
Never use flames near combustible materials.
Use fume hoods as directed.

## Slide 28: Spills…
Immediately clean up any chemicals that you spill.
  Never return spilled or unused material to the reagent bottle.
  Solids should be swept up and placed in the proper was disposal container for that lab.
  Small liquid spills should be diluted with lots of water and mopped up with cloth towel.
  Large spills must be handled by the instructor.

## Slide 29: Caution with Strong Chemicals
Observe caution in using strong chemicals.
Never pour water into concentrated acids; dilute an acid by pouring the acid slowly and carefully into the water with constant stirring.
Use caution in mixing strong acids and bases.

## Slide 30: Smelling Chemicals
When it is necessary to smell chemicals in the lab, the proper technique is to cup your hand above the container and waft the air toward your face.
Try not to breathe in the air through your nose, but bring in just enough to make sense of the smell.

## Slide 31: Injuries

## Slide 32: First Aid…Begin Immediately
Alert the instructor immediately!
If chemicals have come in contact with the eyes, begin eyewashing NOW!
Remove clothes that have chemical contamination
Move everyone away from the area to avoid further contamination

## Slide 33: Injuries…
Chemical spills anywhere on the body:
  Flush the area immediately with large volumes of water from the nearest faucet.
  Remove contaminated clothing if necessary. Use no medication on the injury, but bandage and obtain medical attention if necessary.
Eyes
  Hold the eyes open while flushing for at least 15 minutes at eyewash stations. Obtain medical help immediately.
Concentrated acids or bases spilled over a large body area.
  Use a safety shower, then obtain medical help.

## Slide 34: Fire I
Fire:
Extinguish all burners, remove flammable solvents from the immediate vicinity, and have all people not involved in fighting the fire leave the laboratory by the nearest exit.
Do not attempt to fight a major fire.
Pull the building alarm, shut the windows and fire doors, and leave by the nearest exit.

## Slide 35: Fire II
Clothing on fire:
  Prevent the victim from running.
  Have the victim lie down, and smother the flames with available clothing, a fire blanket, or by rolling the victim around on the ground.
  Towels, books, or other items aflame can be put or pushed in the sink with tongs and doused with water.

## Slide 36: Fire III/Burns
Burns:
  Apply no medication to major burns.
  Cover the area with a sterile dressing and obtain medical help immediately.
  For minor burns, immerse in cold water and bandage when comfortable.

## Slide 37: Cuts & Punctures
Clean your hands and the victim's wound with soap and water, and remove any glass slivers from the wound.
Apply a sterile dressing, and control any severe bleeding by applying pressure directly over the wound.
Apply no medication.
Always obtain medical attention for punctures or severe cuts because of the possibility of tetanus.

## Slide 38: Basic Laboratory Equipment

## Slide 39: Laboratory Equipment I
Students should be familiar with all laboratory equipment.

## Slide 40: Laboratory Equipment II
Students should be familiar with all laboratory equipment.

## Slide 41: Laboratory Equipment III
Students should be familiar with all laboratory equipment.

## Slide 42: Review